## Slide 1: GDS Corp Gas Detection Products For Personnel Protection & Process Monitoring

## Slide 2: Today’s Agenda
Gas Detection System Requirements
Gas and Flame Monitors & Sensors
Display & Alarm Controllers
Process Monitors
Custom Applications
Notes: This training segment will prepare a sales guy to make his initial sales call to a customer.
The slide presentation will be made available to you either on the website or email.
You can modify the presentation to present to your customer.

## Slide 3: Gas Detection System “Must-Have”
Critical Reliability, Plus Best Technology for the Intended Application
Fast Delivery to Meet Real-time Customer Needs
Easy to Use, Easy to Maintain, Easy to Upgrade
Complete Solutions, not Just “Parts”

## Slide 4: Design & Installation Considerations
Why am I taking these measurements? Risk of explosion? Presence of toxic gases?
What are my target gases and related concentrations? Are there gases that interfere or mask the target gas?
What environmental conditions exist that might impact the operation of gas detection equipment? Temperature? Moisture?
How will I deal with maintenance and periodic calibration?

## Slide 5: Essentials of a Gas & Flame Detection System
Display & Alarm Controllers
Solar or UPS Power Supplies
Remote Indication & Display
Gas Detectors
Gas Sensors
Flame Detectors
Notes: There is allot of material to cover. This session will be a full 1 to 1.5 hours.

## Slide 6: Gas Monitors & Gas Sensors
“Gas Monitors” are fully integrated gas detectors that include local or remote sensors, local display and one-person calibration; wired and wireless output
“Gas Sensors” output gas values in mA or ‘direct bridge’ millivolts and require calibration at the controller
“Flame Detectors” monitor infrared, visible and UV spectra for flame signatures
“Sample Draw” systems use pumps or vacuum to pull gas from locations unsuitable for ambient sensors
“Open Path” gas detectors sense the presence of hydrocarbon gas clouds between source and receiver

## Slide 7: GASMAX II DC-Powered Single / Dual Channel Gas Monitor for All Gases
Two channels: one toxic gas sensor and one direct bridge combustible sensor (or 4-20mA)
Graphic LCD shows value and 30 min trend; LEDs provide visual alarm
Non-intrusive “One Person” calibration using magnetic wand
Local Smart Sensors retain calibration constants
Estimates sensor life reading after each calibration
Dual 4-20mA output standard
Options include 5A alarm relays, Modbus® interface, isolated 4-20mA outputs
US
C
Notes: Is the GASMAX/EC loop powered? Yes
What kind of sensors can be used with the GASMAX/EC? EC = electrochemical
The Gasmax II has additional features that are not available on the Gasmax/EC
Two channel GASMAX II.

## Slide 8: GASMAX / EC Loop-Powered Gas Monitor for Toxic Gases
Accepts any GDS Corp toxic gas sensor
Graphic LCD value & trend line
Flashing LED visual alarm indication
Non-intrusive “One Person” calibration using magnetic wand
Local Smart Sensors retain calibration constants & setup data
Supports any GDS Corp EC sensor
Calculates estimated “sensor life” after each calibration
Non-polarized loop output
Available for XP or IS installations
US
C
Notes: Our flag ship product is the GASMAX/EC and GASMAX II.
We have added an important feature to both. This feature allows customers to manage assets [sensors] by determining the when to replace the sensors.
What does “One Man” calibration mean?
We will get into the calibration of GASMAX during the next training session.

## Slide 9: GASMAX / EC Loop-Powered Gas Monitor for Toxic Gases
Oxygen (O2)
Carbon Monoxide (CO)
Chlorine (CL2)
Chlorine Dioxide (CLO2)
Hydrogen (H2)
Hydrogen Sulfide (H2S)
Hydrogen Cyanide (HCN)
Hydrogen Chloride (HCL)
Hydrogen Fluoride (HF)
Sulfur Dioxide (SO2)
Ammonia (NH3)
Ozone (O3)
Ethylene Oxide (C2H4O)
US
C
Silane (SiH4)
Fluorine (F2)
Phosgene (COCL2)
Hydrazine (N2H4)
Nitric Oxide (NO)
Nitrogen Dioxide (NO2)
Mercaptan (TBM)
Tetrahydrothiophene (THT)
Diborane (B2H6)
Notes: Our flag ship product is the GASMAX/EC and GASMAX II.
We have added an important feature to both. This feature allows customers to manage assets [sensors] by determining the when to replace the sensors.
What does “One Man” calibration mean?
We will get into the calibration of GASMAX during the next training session.

## Slide 10: GASMAX II DC-Powered Single / Dual Channel Gas Monitor for All Gases
US
C
All toxic gases shown for GASMAX / EC plus:
Methane (CH4)
Propane
Butane
Pentane
Ethane
Hexane
Propene
Ethylene
Ethanol
Gasoline
Diesel
Acetone
MEK
Styrene
Methane (volume)
Propane (volume)
General hydrocarbons
Benzene
Toluene
Xylene
General VOCs
Carbon Dioxide ppm
Carbon Dioxide (volume)
Others
GASMAX II plus GDS-IR Infrared Sensor
Notes: Is the GASMAX/EC loop powered? Yes
What kind of sensors can be used with the GASMAX/EC? EC = electrochemical
The Gasmax II has additional features that are not available on the Gasmax/EC
Two channel GASMAX II.

## Slide 11: TRANSMAX / EC & II GDS Corp Gas Monitor for General Purpose Areas
Loop-powered and DC-powered gas monitors for general purpose areas
Same electronics and features as GASMAX monitors, but in NEMA 4X non-metallic enclosure
Lightweight Delrin® sensor head with disposable sensor (stainless head also available)
Analog, MODBUS and relay output
Notes: Our flag ship product is the GASMAX/EC and GASMAX II.
We have added an important feature to both. This feature allows customers to manage assets [sensors] by determining the when to replace the sensors.
What does “One Man” calibration mean?
We will get into the calibration of GASMAX during the next training session.

## Slide 12: GASMAX / ECx Battery-Powered Wireless Gas Monitor for Toxic Gases
License-free 900Mhz or 2.4Ghz Wireless Modem transmits data when gas is present*
Internal Lithium battery provides an estimated 6 months of operation under normal conditions (no alarms)
Full graphical interface with 30 min trend display, event log and more
Supports any GDS Corp EC sensor
Non-intrusive “One Person” calibration using magnetic wand
Interface to C1, C64 or C2 Quad Protector Controller with wireless modem
* Sensor operates continuously; microprocessor reads sensor on 6 second intervals and transmits data if alarm condition exists; transmits ‘keep alive’ signal on 5 minute intervals
Battery-powered Infrared Combustible in 2H ‘13

## Slide 13: GASMAX IIx DC-Powered Wireless Gas Monitor for All Gases
License-free 900Mhz or 2.4Ghz Wireless Modem transmits data when gas is present*
Supports any GDS Corp toxic, bridge or 4-20mA output sensor (single channel only)
Full graphical interface with 30 min trend display, event log and more
Non-intrusive “One Person” calibration using magnetic wand
Interface to C1, C64 or C2 Quad Protector Controller with wireless modem
* Sensor operates continuously; microprocessor reads sensor on 6 second intervals and transmits data if alarm condition exists; transmits ‘keep alive’ signal on 5 minute intervals

## Slide 14
Highly reliable dual wavelength design with calibrated 4-20mA output
Five year warranty on sensor; twelve year warranty on IR source
Available with flow cell for process monitoring applications
Combine with GASMAX II for display, alarms, relays and MODBUS®
CSA C22.2 No. 152 Performance Tested Approved for Class 1 Division 1, Groups B, C, D
Suitable for use in SIL-2 systems
GDS-IR Infrared Sensor
Stand-alone Infrared Combustible & CO2 Gas Sensor

## Slide 15
GDS-50 DC-Powered Remote Infrared Combustible & CO2 Sensor Transmitter
Remote sensor transmitter for GDS Corp SmartIR infrared sensors
Standard 3-wire 4-20mA output
Sensors for methane, propane, hydrocarbons and carbon dioxide
Field-replaceable sensor modules
Receiving device must provide for zero and span calibration adjustment
Easy interface to all GDS Corp. alarm and display controllers

## Slide 16
GDS-49 Loop-Powered Remote Toxic Sensor Transmitter
Remote sensor transmitter for all GDS Corp electrochemical sensors
Standard 2-wire 4-20mA output
CSA certified for Explosion Proof or Intrinsically Safe installations
Field-replaceable sensor modules
Receiving device must provide for zero and span calibration adjustment
Easy interface to all GDS Corp. alarm and display controllers
US
C

## Slide 17
GDS-48 Direct Bridge Remote Sensor
Remote sensor for catalytic bead, photoionization and SmartIR infrared sensors
3-wire “direct bridge” output (not 4-20mA)
Sensors for all hydrocarbons, most volatile organics including benzene and toluene, and carbon dioxide
Field-replaceable sensor modules
NOTE: Receiving device must provide for zero / span calibration adjustment
Interface to all GDS Corp. alarm and display controllers configured for ‘direct bridge’ input
US
C

## Slide 18
SharpEye® Flame Detectors
Self-Contained Flame Detectors for Critical Applications
Triple Spectrum design for long distance detection and highest immunity to false alarms
Detects 0.1m2 gasoline pan fire at 65 meters in less than 5 seconds
SharpEye 40/40I
SharpEye 40/40L/LB
UV / IR design for long distance detection and high immunity to false alarms
Detects 0.1m2 gasoline pan fire at 15 meters in less than 5 seconds
Detects hydrocarbon, hydroxyl fuels, metal and inorganic fires
Contact GDS Corp for additional flame detector options

## Slide 19: GDS-58XP Sample Draw System Self-Contained Sample Draw for Hazardous Areas
Designed to pull from wet / dirty locations where ambient sensor will not work.
Long life brushless 24VDC sample pump with built-in low flow warning switch
Adjustable flow meter visually confirms flow
GASMAX II gas monitor supports all GDS Corp toxic or combustible sensors*
Sample lines up to 100m / 300 ft in length
Dual programmable 5A alarm relays and MODBUS output standard
Prompted calibration procedure and built-in Run / Cal valve for easy maintenance
Flowmeter
Inlet & Run / Cal Valve
GASMAX
Monitor
Sensor & Flow Cell
DC Sample Pump

## Slide 20: Display & Alarm Controllers
Central point of display & control for entire gas detection system
Easy access to alarm values and settings
Input signal conditioning for a wide range of sensors and devices
Calibration for low cost sensor transmitters
Programmable relay output logic for system optimization, includes Voting, Zones and Channel / Relay Overrides*
Excitation power for remote sensors and monitors
Simplified interface to plant-wide control systems

## Slide 21: “C2 Quad Protector” Controller Four Channel Display & Alarm Controller
Input 4 analog, 4 direct bridge, 2 analog / 2 bridge inputs or wireless
Graphic LCD displays input values, bar graph and trend data
Three independent alarm levels for each channel
Two standard common alarm relays + six optional discrete relays
Modbus® Interface slave port
117VAC or 24VDC power
Optional 50W external power supply
Class I Division 2 rated for hazardous areas
Notes: C1 is sixteen channel: 8 and 8. All sixteen can be the same type of signal or you can divide the channels into 8 channel segments:
C2 mix and match signal inputs.

## Slide 22: “C2 Protector” Controller Two Channel Display & Alarm Controller with Local Sensors
Input two local toxic sensors, one direct bridge + one toxic, two direct bridge or two 4-20mA
Direct bridge sensors local or remote
Graphic LCD displays input values, bar graph and trend data
Three independent alarm levels for each channel
Two standard common alarm relays + six optional discrete relays
MODBUS® Interface slave port
Class I Division 2 rated for hazardous areas
Notes: C1 is sixteen channel: 8 and 8. All sixteen can be the same type of signal or you can divide the channels into 8 channel segments:
C2 mix and match signal inputs.

## Slide 23: “C1 Protector” Controller 8 or 16 Channel Controller with Analog, Bridge & MODBUS Inputs
Analog input from GASMAX, GDS-IR, GDS-49, GDS-50 or any other 4-20mA device
Direct bridge input for Catalytic bead, SmartIR, or Photoionization Detector
Wireless input for GASMAX/ECx, GASMAX/IIx
Graphics LCD plus 3x LED per channel
Four common relays plus up to 48 discrete
RS-485 MODBUS Master and Slave port
Access via Ethernet with ProtectorView
Class I Division 2 rated for hazardous areas
Notes: C1 is sixteen channel: 8 and 8. All sixteen can be the same type of signal or you can divide the channels into 8 channel segments:
C2 mix and match signal inputs.

## Slide 24: “C1 Protector” Controller 8 or 16 Channel Controller with Analog, Bridge & MODBUS Inputs
4-20mA
Wireless
MODBUS
4X Programmable Alarm Relays
MODBUS RS-485 slave port
Up to six 8-channel discrete relay boards
Ethernet (with external C1D2 module)
Up to 16 Sensors
Input source selectable on per-channel basis
Bridge
Notes: C1 is sixteen channel: 8 and 8. All sixteen can be the same type of signal or you can divide the channels into 8 channel segments:
C2 mix and match signal inputs.

## Slide 25: ProtectorView Software for Windows® Remote Display for Up to Ten C1 Protector Controllers
Monitor C1 controllers across any Ethernet network
Includes Class I Div 2 MODBUS/TCP interface module for C1 controller and remote ProtectorView host software
View one controller in real time while monitoring up to 9 more for alarm conditions
View alarm status and settings in easy-to-read format
Upload and store to disk controller’s internal 24 hour trend database
Ethernet Network

## Slide 26: ProtectorView Software for Windows® Remote Display for Up to Ten C1 Protector Controllers
Color coded BARGRAPH screen shows all sixteen channels
CHANNEL DISPLAY screen shows channel trend, value min & max
CHANNEL HISTORY screen shows downloaded 24hr trend from controller
LED status indicators mirror function on C1 in real time
SENSOR LIFE screen shows 16x sensor life data from most recent calibrations
CONFIG screens show current alarm settings for all sixteen channels
MONITOR WARNING message if monitored C1s indicate alarm

## Slide 27: “C64 Protector” Controller 16 to 64 Channel Controller with Analog, Bridge & MODBUS Inputs
Up to 64 input channels for analog, direct bridge, MODBUS®, wireless or discrete
Full color graphic display with flashing alarms
Five common relays plus up to 256 discretes
Up to four RS-485 MODBUS serial ports
Built-in Ethernet & web page with remote setup
Programmable via voting, zones & overrides
Data logging capability built-in
Class I Division 2 rated for hazardous areas

## Slide 28: “C64 Protector” Controller 16 to 64 Channel Controller with Analog, Bridge & MODBUS Inputs
Main Data Screen shows all 64 channels status and tag names; flashing alarm indication
Bargraph Screen shows 16 channel values, alarms levels and alarm status
Zone screen changes color and name field flashes to indicate alarms
Combination screen shows single channel 30 minute trend, bargraph and large display

## Slide 29: “C64 Protector” Controller 16 to 64 Channel Controller with Analog, Bridge & MODBUS Inputs
4-20mA
Wireless
MODBUS
Up to 64 Sensors
Input source selectable on per-channel basis
Bridge
5X Programmable Alarm Relays
4x MODBUS RS-485 master or slave ports
Up to sixteen 16-channel discrete relay boards (256 total)
Built-in Ethernet with Web Server and Remote Setup
Notes: C1 is sixteen channel: 8 and 8. All sixteen can be the same type of signal or you can divide the channels into 8 channel segments:
C2 mix and match signal inputs.

## Slide 30: Process Monitors
Cost-effective solution where analyzer-level accuracy is not required
Combine high quality sample conditioning / filtering with reliable GASMAX gas monitor and Protector controller technology.
Semi-custom design allows build-to-requirements efficiency
GDS Corp experience in process monitors

## Slide 31: GDS-68XP Process Monitor For Low Oxygen Process Streams
Monitors Hydrogen Sulfide, Mercaptan or THT in 100% methane or methane + carbon dioxide streams
Reliable, low cost toxic sensors and microprocessor-controlled sequencer for low total cost of ownership.
Periodic sampling at intervals from 5 minutes to six hours increases sensor life and reduces amount of target gas released to the atmosphere
Automatic over-range detection protects sensor from saturation
High quality 24VDC brushless pump
Suitable for use in Class I Division 1 areas
Available with ambient sample draw or high pressure inlet with stainless steel filter and regulator
Ideal for use on natural gas pipelines or biogas digesters

## Slide 32: GDS-78XP Process Monitor For High Pressure Process Streams
Semi-custom solution for monitoring a process gas stream compatible with the target toxic or infrared sensor
High quality sample conditioning with stainless steel coalescing filter or optional combination coalescing + membrane filter for maximum moisture & particulate removal.
Choice of two-wire, three-wire or wireless GASMAX gas monitor
Choice of Toxic*, PID or GDS-IR Infrared sensors, or GDS-IR-PM process analyzer sensor
Optional low flow warning switch
Designed for use in Class I Division 1 areas
* Stream must contain at least 25% oxygen for toxic sensor applications

## Slide 33: GDS Corp Custom Systems Design / Build Systems for Petrochemical & Offshore
Design-to-order based on specific customer needs
Unique, one-of-a-kind applications
Contact GDS Corp for more details or a quote
160 point direct catalytic bead system for control of plant-wide deluge system
32 point mixed catalytic bead / infrared system to monitor combustibles and carbon monoxide levels at national research laboratory

## Slide 34
Reliable technology
  Industry-recognized certifications
  Features that customers need today
  Technology for tomorrow’s systems
Fast delivery
  Products designed for rapid build-to-order
  Locally managed inventory
  Software tools simplify ordering
Easy to use
  Graphical interface
  Smart sensors
  Prompted Calibration
Complete solutions
  Monitors, sensors, controllers, power supplies, software & more

## Slide 35
For More Information: www.gdscorp.com

## Slide 36
Thank You!

## Slide 37: GDS Corp Sensor Technologies

## Slide 38: Gas Sensor Technologies
Toxic
Infrared
Catalytic Bead
Photoionization (PID)
Diffusion Barrier
Electrolyte
Storage
Sensing Electrode
Active Bead
Reference Bead
Infrared Light Source
Infrared Detector
Target Gas Absorbs IR Energy
Target Gas Reacts with Electrolyte, Generates Current
Target Gas Generates Heat, Causing Imbalance
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector

## Slide 39: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Diffusion Barrier
Electrolyte
Storage
Sensing Electrode
Active Bead
Reference Bead
Infrared Light Source
Infrared Detector
Target Gas Absorbs IR Energy
Target Gas Reacts with Electrolyte, Generates Current
Target Gas Generates Heat, Causing Imbalance
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector
Toxic

## Slide 40: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Diffusion Barrier
Electrolyte
Storage
Sensing Electrode
Infrared Light Source
Infrared Detector
Target Gas Absorbs IR Energy
Target Gas Reacts with Electrolyte, Generates Current
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Toxic

## Slide 41: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Diffusion Barrier
Electrolyte
Storage
Sensing Electrode
Infrared Light Source
Infrared Detector
Target Gas Absorbs IR Energy
Target Gas Reacts with Electrolyte, Generates Current
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Toxic

## Slide 42: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Diffusion Barrier
Electrolyte
Storage
Sensing Electrode
Target Gas Reacts with Electrolyte, Generates Current
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Longer sensor life
Does not require Oxygen to detect combustibles
Bridge output signal (except GDS-IR)
Examples: Combustibles, CO2
Toxic

## Slide 43: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Diffusion Barrier
Electrolyte
Storage
Sensing Electrode
Target Gas Reacts with Electrolyte, Generates Current
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Longer sensor life
Does not require Oxygen to detect combustibles
Bridge output signal (except GDS-IR)
Examples: Combustibles, CO2
Toxic

## Slide 44: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
Current Detector
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Longer sensor life
Does not require Oxygen to detect combustibles
Bridge output signal (except GDS-IR)
Examples: Combustibles, CO2
Wide range of specific target gases
Sensor life determined by environmental factors (%RH, ambient gases / poisons)
Requires Oxygen to function
Micro-amp output signal
Examples: H2S, O2, CO
Toxic

## Slide 45: Gas Sensor Technologies
Infrared
Catalytic Bead
Photoionization (PID)
Ultraviolet Light Source
+
UV Ionizes Target Gas, Creating Current
e-
e-
Current Detector
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Longer sensor life
Does not require Oxygen to detect combustibles
Bridge output signal (except GDS-IR)
Examples: Combustibles, CO2
Wide range of specific target gases
Sensor life determined by environmental factors (%RH, ambient gases / poisons)
Requires Oxygen to function
Micro-amp output signal
Examples: H2S, O2, CO
Toxic

## Slide 46: Gas Sensor Technologies
Catalytic Bead
Photoionization (PID)
Wide range of specific target gases
Sensor life determined by environmental factors (%RH, ambient gases / poisons)
Requires Oxygen to function
Micro-amp output signal
Examples: H2S, O2, CO
Longer sensor life
Does not require Oxygen to detect combustibles
Bridge output signal (except GDS-IR)
Examples: Combustibles, CO2
Infrared
Lowest cost / periodic replacement required
Oxygen MUST BE PRESENT to detect combustibles
Bridge output signal
Examples: Methane, Hydrogen, Combustibles
Wide range of detectable gases (determined by energy of UV lamp)
Not specific to particular VOC component
Bridge output signal
Examples: Benzene, Gasoline, Volatile Organic Compounds (VOC)
Toxic

## Slide 47: Toxic & Combustible Gas Detection

## Slide 48: Combustible Gas Detection
Combustible gas is measured on the basis of “Percent (of) Lower Explosive Limit, or %LEL of a specific target gas
LEL values for most gases are well known and alarm values can be readily calculated for maximum safety
Generally, alarm values are set for 20% LEL (high alarm) and 40% LEL (high-high alarm), but may vary based on gas and risk
Most combustible gas sensors are not specific and will respond to any combustible gas
Infrared sensors will not detect hydrogen

## Slide 49: Combustible Gas Detection
LEL
UEL
0% by Volume
100% by Volume
“Upper Explosive Limit”
“Lower Explosive Limit”

## Slide 50: Combustible Gas Detection
LEL
UEL
0% by Volume
100% by Volume
“Upper Explosive Limit”
“Lower Explosive Limit”
Insufficient gas to support combustion

## Slide 51: Combustible Gas Detection
LEL
UEL
0% by Volume
100% by Volume
“Upper Explosive Limit”
“Lower Explosive Limit”
Insufficient gas to support combustion
Insufficient oxygen to support combustion

## Slide 52: Combustible Gas Detection
LEL
UEL
0% by Volume
100% by Volume
“Upper Explosive Limit”
“Lower Explosive Limit”
Insufficient gas to support combustion
Insufficient oxygen to support combustion
Any mixture in this range WILL support combustion

## Slide 53: Combustible Gas Detection
LEL
UEL
Gasoline UEL = 7.1%
Gasoline LEL = 1.2%
Combustible gases have different values for LEL and UEL

## Slide 54: Combustible Gas Detection
LEL
Combustible gases have different values for LEL and UEL
An unknown mixture of combustible gases may have a unique LEL
Ethylene Oxide UEL = 100%
Ethylene Oxide LEL = 3.6%

## Slide 55: Combustible Gas Detection
LEL
UEL
Combustible gases have different values for LEL and UEL
An unknown mixture of combustible gases may have a unique LEL
Methane (CH4) is often used as a reference for calibration purposes
Methane UEL = 15%
Methane LEL = 5%
0 – 100% LEL

## Slide 56: Toxic Gas Detection
Toxic limits are based on tests and recommendations from OSHA* and NISOH*
IDLH (Immediately Dangerous to Life or Health) specifications based on human & animal toxicity, 10% of LEL, effects of similar known chemicals and historic norms
Exposure is measured in instantaneous and average values; Averages must be calculated from GDS Corp equipment readings
NIOSH: US National Institute for Occupational Safety and Health
OSHA: US Occupational Safety and Health Administration

## Slide 57: Toxic Gas Exposure Limits
Ceiling Exposure Limit - CEV
(Maximum exposure at any time)

## Slide 58: Toxic Gas Exposure Limits
Short Term Exposure Limit - STEL
(Average exposure over 15 minutes)
Ceiling Exposure Limit - CEV
(Maximum exposure at any time)

## Slide 59: Toxic Gas Exposure Limits
Time-Weighted Average - TWA
(Average exposure over 8 hours)
Short Term Exposure Limit - STEL
(Average exposure over 15 minutes)
Ceiling Exposure Limit - CEV
(Maximum exposure at any time)

## Slide 60: Toxic Gas Exposure Limits
Time-Weighted Average - TWA
(Average exposure over 8 hours)
Short Term Exposure Limit - STEL
(Average exposure over 15 minutes)
Ceiling Exposure Limit - CEV
(Maximum exposure at any time)
CEV = 12 ppm

## Slide 61: Toxic Gas Exposure Limits
Time-Weighted Average - TWA
(Average exposure over 8 hours)
Short Term Exposure Limit - STEL
(Average exposure over 15 minutes)
Ceiling Exposure Limit - CEV
(Maximum exposure at any time)
CEV = 12 ppm
STEL = 2 ppm

## Slide 62: Toxic Gas Exposure Limits
Time-Weighted Average - TWA
(Average exposure over 8 hours)
Short Term Exposure Limit - STEL
(Average exposure over 15 minutes)
Ceiling Exposure Limit - CEV
(Maximum exposure at any time)
CEV = 12 ppm
STEL = 2 ppm
TWA = 0.05 ppm